## Slide 1: Real-Time Audio Classification for Arduino Car Control
Recognising Keywords and Using them to control an Arduino Car

## Slide 2
This project explores the integration of audio classification to control an Arduino car using voice commands. The primary goal is to create a user-friendly interface that enables hands-free operation of the vehicle.
Key Features
Voice Input: Commands will be captured using a microphone. The audio input will be processed and recognized before being transmitted to the car for execution.
Command Set: Users can issue commands such as "forward“, "left“, "right“, “up“, “down“, or “stop" to control the car's movement and direction.
Practical Application
This project demonstrates the practical applications of audio processing and classification, showcasing how voice commands can enhance user interaction with robotic systems.
Project Overview-

## Slide 3: Main Objectives-
Real-Time Audio Processing: Convert audio data into spectrograms using Short-Time Fourier Transforms (STFT), which retain time information in the transformation from time-domain signals.
Spectrogram Classification: Use a Convolutional Neural Network (CNN) to classify the spectrogram images, trained on audio samples of people speaking commands.
Practical Application Demonstration: Showcase how audio processing and classification can be applied in robotics to enhance user interaction.

## Slide 4
Arduino Car Overview-
Components Used-
Arduino Board
Motor Driver Modules
DC motors
Battery Pack
Bluetooth Module
Movement Instructions-
Left: Turns Left
Right: Turns Right
Up: Moves Forward
Down: Moves Backward
Stop: Stops Car

## Slide 5
Dataset Overview-
We use mini speech commands dataset a smaller version of the Speech Commands dataset. The original dataset consists of over 105,000 audio files in the waveform (WAAV) audio file format of people saying 35 different words.
Each word has 1000 files we use 800 for training and 200 for validation of each
Data Preprocessing –
The data is first trimmed to 1sec and set to 16KHz sampling rate
Then is converted to spectrograms using STFT the time domain signal is converted into windows and the Fourier transform of each is calculated and represented in a matrix
Dataset Overview and Data Preprocessing-

## Slide 6
TensorFlow-
TensorFlow is an open source machine learning framework developed by google
It is used to design and build models including audio classification
TensorFlow provided the framework for building the model and allowed us to build a simple neural net for audio classification
It allowed us to easily normalise and process the data we got allowing the model to learn efficiently
It provides build in optimisers and loss functions

## Slide 7
Real Time Microphone Input-
We use the PyAudio library to interact with the computer's microphone and audio system. It allows us to open a stream to capture real-time audio data.
We specify audio settings such as sampling rate (16KHz), format and buffer size. These settings control how we record the audio.
We create an input audio stream, which starts recording audio in real time, capturing small chunks of audio data continuously.
The waveform is normalized and converted into a spectrogram, which is the format used by the model for making predictions.

## Slide 8
Our Members-
Dheeran Sankaran
Joshua Edwin
Johan Emmanuel
Aditya